## Slide 1: Display Builder Tutorial
Jan. 2020
Kay Kasemir, kasemirk@ornl.gov

## Slide 2: Changes
Jan. 2019 USPAS: Initial version
Jan. 2020 Class file details

## Slide 3: Display Builder
Operator Interface Editor and Runtime
Builds on ideas from EPICS edd/dm, medm, edm, ..
Very compatible with CS-Studio ‘BOY’
Started ~2015 in CS-Studio/Eclipse, now in CS-Studio/Phoebus

## Slide 4: Examples: SNS Accelerator
CS-Studio ‘BOY’ *.opi files

## Slide 5: Examples: SNS Beam Lines

## Slide 6: Browse the Examples
Start CSS/Phoebus
Your setup might have a menu entry
  File, Top Resources, Examples
If not, or if you’d like to inspect and edit the examples
  Applications, Display, Examples, Install Example Displays
Main Application Toolbar Menu Window, Show Toolbar
Example Display Push any of the buttons
Display Runtime Toolbar Context Menu Window, Show / Hide Toolbar
Navigate back/forward also via Alt-Left, Alt-Right cursor keys Zoom to view large control room displays on office computer
Tab Hover mouse, open Context Menu, Close
Context Menu Details change with widget on which menu was invoked

## Slide 7: Send PV to other Tools
Context menu opens other tool with PV

## Slide 8: Open Existing Display In Editor
Context menu can open any display in Editor
Downloads remote files

## Slide 9: Create New Display
Menu Applications, Display, New Display
  Enter a name with .bob file extension
Main Editor Area Select Widgets Move, resize widgets Ctrl-C, V, X to copy, paste, delete (⌘ on Mac)
Save & Execute the Display
Property Panel Edit properties of selected widgets

## Slide 10: Editing a Display
Quick Edit Double-click widget to
a) Edit text of Label
b) Edit PV of widgets that use a PV
Widget Palette Drag widget into editor
- or -
1) Select Widget Type
2) Draw rectangular area in display
Selecting Widgets a) Click single widget
b) Ctrl-click to add widget (⌘ on Mac)
c) Drag ‘rubberband’ around widgets
d) Click or Ctrl/ ⌘ click in widget list

## Slide 11: Suggested Setup for Editing
Pick a top directory, for example where you installed the example files
Open Applications, Utility, File Browser
  Set it to your top directory
  On file browser tab, open context menu, “Split Horizontally”, then “Lock Pane”
Menu Window, Save Layout As..
  “Editing”
Menu Applications, Display, New Display
  Create new file in your top directory
File Browser Set to your “top” directory.
Locked.
Edit vs. Run a) Double-click to run.
b) Right-click, Open With.., Editor

## Slide 12: Keep It Simple
Add a Widget
Enter Label’s Text or Widget’s PV Name
Done
At Runtime, widget will
Show PV’s value, formatted, with units
Indicate alarm, disconnect
Show tool-tip with PV name and value
Combo options read from Enum PV, slider range from numeric PV
Disabled when ‘control’ widget has no PV write access

## Slide 13: Extend the First Display
Drag a “Text Update” from the palette
  Enter PV name “sim://ramp(1, 10, 1)”. Note PV name auto-completion popup.
Add “Boolean Button”
  PV name “loc://test”
Add “LED”
  PV name “loc://test”. Note name in PV History.
Execute the display
  Toolbar Button or Context Menu

## Slide 14: PV Names
ca://some_pv_name
  EPICS Channel Access PV
some_pv_name
  Typically same, since “ca://” is the default
sim://sine
  Simulated PV. See auto-completion hints
loc://x(4)
  Local PV. See auto-completion hints
pva://x
  EPICS pvAccess

## Slide 15: Widget Palette
Shows all available widgets
  Enter name for ”Search”
  Hover mouse for description
  Drag -or- Select & Rubberband
Categories
  Graphics show static label, picture, ..
  Monitors update based on reading a PV
  Controls read a PV and can write to the PV
  Plots tend to read from one or more (waveform) PVs
  Structures group widgets, embed sub-displays

## Slide 16: Create Widgets via Drag/Drop from other Apps
Email with list of PVs?
  Drag that text into Display Editor
  Select widget type
Supported:
  Text  Label
  Text  PV Widget
  Image File  Picture Widget
  *.bob File  Embedded Display Widget

## Slide 17: Manipulating Widgets
Widget List Select widgets
Rename Widgets
View/change their order.
Selected Widgets Tracker Move or resize selected widgets
Snap to Grid
.. Other Widgets
Show Coordinates
Order
Front/Back
Align
Size
Distribute

## Slide 18: Display Properties
Click on display background to select no widget for editing overall display properties
Name
  Shown in Tab
Macros
  Used by all widgets in this display
Grid size
  Can aid with placing widgets

## Slide 19: Widget Properties
Select one (or more) widgets to edit their (common) properties
Search
  To find desired property
PV Name
  Most important property for most widgets
Details depend on the widget type

## Slide 20: Common Widget Properties
Defaults tend to be reasonable:
  Format with precision set by PV
  Show units provided by PV
  Alarm-sensitive Border
  Fetch Items (Combo, …) from PV
  Instead of changing them, maybe the PV needs to be updated?
  Still, can be adjusted as needed for the display.

## Slide 21: Predefined “Named” Colors and Fonts
Use whenever possible!

## Slide 22: Configuring Named Colors, Fonts
Ideally set at start of project

## Slide 23: Widget Notes
Text Entry, Text Update:
  Set Format = String for “long string” waveforms. Default will show array.
LED, Boolean Button, Checkbox
  Boolean PV
  Numeric PV 0 or not 0 (when ”Bit” set to default of -1)
  Bit in a numeric PV (when ”Bit” set to 0, 1, 2, …)
Multi-State LED
  Enumerated or numeric PVs
  Defaults to using state values 0, 1, 2, 3, ..

## Slide 24: Widget Notes
Combo Box, Radio Button:
  Best for enumerated PV: Enter PV name, done
  Alternatively, un-check “Items from PV” and enter items

## Slide 25: Action Button
Add ActionButton
Configure “Actions” property, add “Open Display”
Run: Clicking button opens the “other” display.
In principle, any widget can have ‘Actions’. They appear in the widget’s runtime context menu. But it’s not obvious to end users that for example a Label will have actions.

## Slide 26: Screen Navigation
Replace
  Suggested default.
  Allows back/forward navigation as in web browser
  Minimizes number of open screens
New Tab
  Opens in new tab
  Allows specific Pane name
New Window
  Opens in new window
With “Replace”, can still use
  Context menu
  Control (⌘ on Mac) for tab
  Shift-Control for window

## Slide 27: Screen Navigation: Tabs
Tabs
Each tab is in-memory, same *.bob
Appears immediately when selected
Uses CPU and memory when hidden
Navigation Tabs
Tab is loaded from separate *.bob when selected
May need a little time to load
No CPU and memory when hidden

## Slide 28: Macros
Macros are passed into displays from
  Enclosing Group or Tab Widget
  Display
  Embedded widget container or Action that loaded the display
  Phoebus preferences
To use: $(NameOfMacro)
Examples:
  PV Name: $(PV) with PV=TheFullPVName
  PV Name: Motor$(N) with N=1, 2, 3, …
  Width: $(WID) with WID=200
  Visible: $(SHOW) with SHOW=true
.. or ${NameOfMacro}.
EPICS *.db files use $(xx), SNL and shell use ${xx},
so we support both conventions.

## Slide 29: Macro Example
Create display “sub.bob”
  Label with text “Motor $(N)”
  TextUpdate with PV “loc://pos$(N)(10)”
  ActionButton with PV Name “loc://pos$(N)(10)” and Action to “Write PV” value 20
  Copy that button, update to set PV to 30
Create display “top.bob”
  ActionButton with Action to open sub.bob with N=1
  Copy/paste the button, update to N=2
Execute top.bob, press buttons
sub.bob
“Motor $(N)”
sub.bob
“Motor 1”
sub.bob
“Motor 2”
top.bob
N=1
N=2

## Slide 30: Macros
Default values: $(MACRO=default)
  Allows standalone testing without passing values into display
To enter macro for Boolean
  Press the “$” macro button
  Select valid option from drop-down …
  .. or enter a macro

## Slide 31: Macro Fallbacks
When macro is not defined, falls back to
  Widget Properties
    Uses the internal property name shown in tool-tip of Properties view
    Note how tooltip is usually preset to “$(pv_name)\n$(pv_value)”
    Action Button has PV Name property. It’s not used directly as in other widgets with PV name, but in “Write PV” the PV name is preset to $(pv_name)
    Action Button text is preset to “$(actions)”
  Java Properties
    $(os.name)
  Environment Variables
    $(HOME), $(USER)

## Slide 32: Predefined Macros
  $(DID): Unique display identifier, useful for per-display PVs
  loc://x$(DID)(10)
  $(DNAME): Display Name

## Slide 33: Group Widget
Contains other widgets
Visual Effect:
  Border, Name
Practical Effect:
  Group can define macros for contained widgets
  Group can be moved, copied/pasted as one unit in editor

## Slide 34: Group Widget
1) Add Group Widget
2) Move other widgets inside the Group
Active Group is highlighted

## Slide 35: Group Properties
Name: Shown in border
Style: “Group Box” for named border
Macros: Passed to contained widgets

## Slide 36: Group Editing Shortcuts
Select Widgets
Context menu “Create ..”
Select Group
Context Menu “Remove..”

## Slide 37: Embedded Display
Hosts a complete *.bob file within a widget
Allows composing higher-level displays from smaller displays:
  Per-device *.bob
  Show multiple devices in one display

## Slide 38: Embedded Display Example
Create display “sub.bob” (or use the one created earlier)
  Label with text “Motor $(N)”
  TextUpdate with PV “loc://pos$(N)(10)”
Create display “main.bob”
  Embedded Display, File sub.bob, Macros N=1
  Copy/paste the Embedded Display, update to N=2
Execute main.bob
sub.bob
“Motor $(N)”
main.bob
N=2
sub.bob
“Motor 1”
N=1
sub.bob
“Motor 1”

## Slide 39: Embedded Display Sizes
Embedded Display Size
  Size of the widget that will host the *.bob
  Defined by the widget Width and Height properties
Content Size
  Size of the *.bob
  Defined by that Display Width and Height properties
What if those sizes differ?

## Slide 40: Embedded Display Resize Options
No Resize
Size content to fit widget
Size widget to fit content
No Resize usually best. Scrollbars appear as needed.
Resizing results in odd font sizes or widgets that outgrow their initial space.

## Slide 41: Embedded Display Editing

## Slide 42: Top Resources
See Help, Preference Settings
Start phoebus with “-settings /path/to/my_settings.ini”:
  org.phoebus.ui/top_resources=/home/controls/displays/main.bob, Start Page | http://controls.my.site/displays/main.bob, Start Page
  File system: Use NFS or ‘git pull’ to distribute files
  http: All users always see the same set of files

## Slide 44: Many Widgets and Properties
Compared to earlier EPICS display tools,
  Group Widget instead of Lines
  LED instead of Circle-with-changing-color
  Tab/Navigation Tabs instead of buttons, local PVs, conditional visibility,..
Display describes Meaning:
  Group of related widgets
  LED for binary PV, not circle that happens to change color
Files with meaning are easier to translate into the next tool

## Slide 45: Widget Classes
Instead of creating a Label with large font, define a “TITLE” class for the Label
Instead of creating an LED with Orange color, define a “WARNING” LED class

## Slide 46: Editing *.bcf Widget Class Files
Name Defines a widget Class:
‘WARNING’ LED, ‘TITLE’ Label, …
Slightly different editor behavior
Checked Property:
Value becomes part of class definition

## Slide 47: Using Widget Classes
Select Widget Class
Disabled:
Cannot change the class-based property
Class Indicator: Property is handled by class
Context Menu: Re-load classes in case *.bcf is changed while editing display

## Slide 48: Class Details
*.bcf files define widget classes
  Label of class TITLE uses font XYZ
When editing a *.bob file, classes are applied. Add Label, select Class TITLE:
  Font is set to XYZ
  Can no longer change the font
  File is saved with font=XYZ, marked as “use_class”
*.bob files use widget classes, if they are defined. Open a file with Label of class TITLE, and
  TITLE is a known class: Whatever that class defines is used. If it sets font=EFG, that’ll be used.
  TITLE is not a known class: Using font=XYZ as saved in file.

## Slide 49: Compare *.bcf and *.bob to *.css and *.html
*.bcf classes are similar to *.css style settings, *.bob files are similar to *.html content
Have same *.bcf/*.css
   Display looks the same
Use different *.bcf/*.css
   Display looks as requested in my *.bcf/*.css
Have no *.bcf/*.css
  *.html turns into rubbish, lacking any description of what to look like. *.bob display looks as seen by last person who edited it, since the class settings effective at that time are in the *.bob file.

## Slide 50: Rules
Ideally, use widgets’ built-in functionality
  Value of PV displayed in TextUpdate, LED, ..
  Alarm indicated via Border
Sometimes useful to for example hide a widget, i.e. change visibility based on a PV
  Rules can accomplish this
  .. But functionality may not be obvious to the next person who needs to maintain a display

## Slide 51: Adding a Rule
Add TextUpdate widget
Set PV to sim://ramp(0, 10, 1)
Open Widget’s Rules
Add Rule, name it “Hide”
Select “visible” property
Add PV sim://ramp(0, 10, 1)
Add Boolean Expression “pv0>8”
Un-check value
Run

## Slide 52: Rules Detail
Triggered by at least one PV
  May use additional non-trigger PVs
Expressions use pv0, pv1, .., pvStr0, pvStr1, .. to access PVs’ values
Rule internally converted to Jython
  Use preview to debug
“else: ..” sets property to original value

## Slide 53: Scripts
Scripts are attached to a widget
Triggered by at least one PV
  May use additional non-trigger PVs
Invoked with
  pvs[] – Array of requested PVs
  widget – The widget
Script can
  Read & write the received PVs
  Set widget properties
  Locate other widgets in the display
  Invoke any Java code in the product
  Be very powerful
  Result in an unmaintainable mess
One Script Executor per *.bob file, Runs in background thread
  Slow scripts do not block the UI
  One script per display at a time
    Many short-duration scripts
    One that never quits

## Slide 54: Rules vs. Scripts
Both are in the end Jython code
Both should be the exception. Plain displays don’t need them. But can be powerful, replacing separate custom Java/Python/C/C++ applications.
Prefer Rules because they describe meaning, easier to maintain

## Slide 55: When to use a script
It’s simple, well documented, and tremendously improves the UI
Would be a one-of, specialized, hard to maintain, separate application anyway. With a script, at least its integrated into the operator UI
Examples:
Turn scalar PVs into loc://waveform for guideline in XYPlot
Fill display with 50 widgets based on config file, examples/template_and_script
Add information from web service to display

## Slide 56: When not to use a script
It adds logic to the display that should be on the IOC
  Display should only display PVs and allow user to write PVs.
  Display must never do anything
You have to ask for help implementing the script
  If you can’t implement it, you can’t maintain it, either
Examples
Open relieve valve when pressure too high. Ramp Power Supply.
  What if somebody closes the display? Opens two displays?
Wiggle something on the display
  It’s not a video game

## Slide 57: Summary
Display Builder is powerful Editor and Runtime with many Widgets, Macros etc.
Keep it Simple
Add a Widget
Enter Label’s Text or Widget’s PV Name
Done