## Slide 1: PV Access
Oct. 2018
Kay Kasemir
Python examples by Amanda Carpenter

## Slide 2: History
Channel Access
  DBR_*: Numbers, enums, string, scalar and array, with time, alarm, limits
  Since beginning of EPICS
  Still fully supported
PV Access
  PV Data: Arbitrary structures
  Started as “EPICS V4” development
  Since EPICS 7 (Dec. 2017) included in EPICS base

## Slide 3: PV Access
Fundamentally similar to Channel Access
  Name search via UDP
  Connection for data transfer via TCP
  EPICS_PVA_ADDR_LIST, EPICS_PVA_AUTO_ADDR_LIST
Get, put, monitor
  Plus an ‘RPC’ type operation
Arbitrary PV Data structures instead of DBR_.. types

## Slide 4: Custom Data: Great, but then what?
structure: double value short status short severity string units time timeStamp …
structure: short level double data string type time stamp …
structure: short info double content string meta long ms …
Which number to show on a user display?
What units?
Is this an alarm?
Time stamp?
structure: short level double wert string typ long zeit …

## Slide 5: “Normative Types”
Channel Access
struct dbr_ctrl_double: short status short severity short precision char units[8] … no timestamp … double value struct dbr_time_double: short status short severity timestamp stamp double value
You get what you request (network always transfers complete struct)
PV Access
epics:nt/NTScalar: double value short status short severity string units time timeStamp …
You get what you request (but network only transfers changes)

## Slide 6: Channel Access vs. PV Access
EPICS 7 IOCs include PVA server Similar command line tools:
pvinfo training:ai1
pvget training:ai1
pvget –m training:ai1
pvget -r 'field()' training:ai1
pvget training:ai1.SCAN
cainfo training:ai1
caget training:ai1
camonitor training:ai1
caget –d CTRL_DOUBLE training:ai
caget training:ai1.SCAN

## Slide 7: CS-Studio: Use ‘pva://…’

## Slide 8: Images: Normative type NTNDArray
Served by Area Detector (NDPluginPVA) or ‘start_imagedemo’
pvinfo IMAGE
  Value, dimensions, codec
CS-Studio: Image widget
  Only needs pva://IMAGE

## Slide 9: Custom PV Data
SNS Beam Lines started to use this in ~2014
  start_neutrondemo
  pvinfo neutrons
Allows fetching just what’s needed:
  # For detector pixel display pvget -r 'field(pixel)' neutrons pvget –m -r 'field(timeStamp, pixel)' neutrons
  # For energy displays pvget –m -r 'field(time_of_flight, pixel)' neutrons

## Slide 10: Custom PV Data in CS-Studio
Cannot handle arbitrary structure
  pva://neutrons
Can handle fields which are scalar or array
  pva://neutrons/proton_charge
  pva://neutrons/pixel

## Slide 11: PV Access and Python
Basic ‘get’
  cd ~/epics-train/examples/python/
  python example1.py
‘monitor’
  python example2.py

## Slide 12: PV Access API with Channel Access as “Provider”
PV Access supports both the actual PvAccess protocol but also Channel Access.
New tools, written for PVA, can thus fall back to CA:
  python example3.py
Tools like CS-Studio can use both ca:// and pva://, so multiple transition options.

## Slide 13: Custom PV Data in Python Client
Python receives data as dictionary, access to any element
  python neutrons.py

## Slide 14: Custom PV Data from Python Server
Surprisingly easy:
  # Server
  python server.py
  # Client
  pvinfo pair
  pvget -m -r "x, y" pair
pv = PvObject({'x': INT, 'y' : INT})
server = PvaServer('pair', pv)
x = 1
while True:
pv['x'] = x
pv['y'] = 2*x
server.update(pv)
sleep(1)
x = x + 1

## Slide 15: More Examples
Display Builder pva_server_ramp
  Python code that serves ‘pva://ramp’ with alarm, prec, timestamp, …
Display Builder table_server
  Python code that serves ‘pva://table’ as “NTTable”
  Not practical to replace regular IOCs with python, but useful when custom data is needed

## Slide 16: Custom PV Data from IOC Records
`makeBaseApp.pl –t example` includes “group”, see ~/epics-train/examples/ExampleApp/Db/circle.db
  Calc records ..:circle:x & ..:circle:y compute (x, y) coordinate on circle
  info() annotations create PV ”training:circle” PV as struct { angle, x, y }
PVA “training:circle” updates atomically
  camonitor training:x training:y receives separate x, y updates pvget –m training:circle will always see sqrt(x2+y2)==1
  cd ~/epics-train/examples/python python circle.py

## Slide 17: PV Access
Update to Channel Access
  Both can be used in parallel
Similar, but supports custom data types
  Won’t replace IOC, but useful for special cases
Since EPICS 7 included in base
  Details of ‘group’, PVA gateway, ‘field(…)’ access still evolving