## Slide 1: PV Access Introduction
EPICS Collaboration Meeting
Slovenia, Sept. 2022
Kay Kasemir

## Slide 2: What is EPICS?
Network Protocol plays central role
“Integrate into EPICS” = “Make accessible on Network”
Network Diagram
Network Diagram (new)

## Slide 3: EPICS Network Protocols
Channel Access
  Since beginning of EPICS
  DBR_*: Numbers, enums, string, scalar and array, with time, alarm, limits
  Still fully supported
PV Access
  Started as “EPICS V4” development
  PV Data: Arbitrary structures
  Since EPICS 7 (Dec. 2017) included in EPICS base

## Slide 4: History
RSRV Server in IOC, Client in IOC and on Host, K&R C then ANSI-C
PCAS Server for Host, C++
Bindings for tcl, perl, python, matlab, java, …
CAJ (pure Java)
EpicsSharp (pure C#)
Caproto (pure python)
Original
pvData/pvAccess C++ & Java implementation
pvaPy binding
core-pva Java update
Pvxs C++ update
p4p
Channel Access
PV Access
QSRV server for IOC
incomplete, not to scale, to be continued

## Slide 5: First Glance
softIoc vs. softIocPVA
  # Compare CA-only example: cd /ics/examples/02_fishtank cat st.cmd # .. with this one: cd /ics/examples/24_pvaccess cat st.cmd ./st.cmd
pv… instead of ca…
  camonitor training:setpoint training:tank pvmonitor training:setpoint training:tank pvput training:setpoint 40 caput training:setpoint 30
CS-Stud﻿io:
  css -resource /ics/examples/24_pvaccess/pva.bob

## Slide 6: PV Access
Similar to Channel Access
  Name search via
    UDP Broadcast (IPv4), Multicast or Unicast (IPv4, IPv6), configured via EPICS_PVA_ADDR_LIST, EPICS_PVA_AUTO_ADDR_LIST
    TCP search via EPICS_PVA_NAME_SERVERS
  Connection for data transfer via TCP
  Same “channel” or “PV” abstraction from ”record”
Get, put, monitor
  Plus an ‘RPC’ type operation

## Slide 7: Channel Access vs. PV Access
Similar command line tools:
caget training:tank
camonitor training:tank
cainfo training:tank
caget –d CTRL_DOUBLE training:tank # Not supported camonitor –d CTRL_DOUBLE training:tank
caget training:tank.SCAN
pvget training:tank
pvmonitor training:tank
pvinfo training:tank pvget –M raw training:tank
# Note first few updates! pvmonitor –M raw training:tank
pvget training:tank.SCAN

## Slide 8: CS-Studio
Use pva://… prefix to select PV Access
Use ca://… prefix to select Channel Access
Set default in /ics/tools/phoebus/settings.ini

## Slide 9: How to add PVA to IOC?
Use softIocPVA
Start with `makeBaseApp.pl –t example`
Add to your own makeBaseApp-type Makefile: myioc_DBD += PVAServerRegister.dbd myioc_DBD += qsrv.dbd myioc_LIBS += qsrv myioc_LIBS += $(EPICS_BASE_PVA_CORE_LIBS)
Either way adds PVA and keeps CA

## Slide 10: So it’s very similar, maybe more efficient…
What’s really new?
How about those custom structures?

## Slide 11: Custom Data: Great, but then what?
Fred’s structure: double value short status short severity string units time timeStamp …
Keith’s structure: short level double data string type time stamp …
Jane’s structure: short info double content string meta long ms …
Which number to show on a user display?
What units?
Is this an alarm?
Time stamp?
Jürgen’s structure: short grad double wert string typ long zeit …

## Slide 12: “Normative Types”
Channel Access
struct dbr_ctrl_double: short status short severity short precision char units[8] … no timestamp … double value struct dbr_time_double: short status short severity timestamp stamp double value
You get what you request (network always transfers complete struct)
PV Access
epics:nt/NTScalar: double value short status short severity string units time timeStamp …
You get what you request (but network only transfers changes)
Same record vs. PV abstraction.
There is no “NTRecord” or “NTCalcOut” that would fetch all fields of a record

## Slide 13: Reminder: Channels/PVs vs. Records
Records have fields
Channels/PVs have properties
IOC maps fields of records to properties of channel/PV
  VAL  value
  TIME  timestamp
  STAT & SEVR  alarm
  EGU  Units
  PREC  display hints
  HIGH  upper warning threshold
Nearly every record.FIELD can become a PV: caget xxx
caget xxx.VAL caget xxx.EGU Detailed mapping of fields to channel/PV depend on record

## Slide 14: Images: Normative type NTNDArray
Standalone Demo Image cd /ics/examples/24_pvaccess ./start_imagedemo
CS-Studio Image widget
  Only needs pva://IMAGE
  css -resource /ics/examples/24_pvaccess/PVA_IMAGE.bob

## Slide 15: Images: Area Detector
Area Detector with “Sim” and NDPluginPVA cd /ics/examples/AreaDetector ./start_sim_ioc.sh
CS-Studio: Image widget
  Just “pva://….:Image
  ”Limits from PV” option
  css –resource /ics/examples/AreaDetector/0_AreaDetectorDemoPVA.bob

## Slide 16: Area Detector Demo
“Start” Sim Detector, “Enable” PVA Plugin
Open display in editor to check Image widget config
  Simple config via PV Name, maybe Limits from PV option
  Data size, Color Mode, Unsigned are not needed!
Open “Detector” page, change “Region Size”, “Reverse”, “Data Type”
  Image updates accordingly!
Open “Plugins”
  Enable “NDPluginCodec”
    Read SIM1
    Select “LZ4” compressor, note “Compression Factor”
  Set NDPluginPva to use Port “CODEC1”
  Verify via `pvget 13SIM1:Pva1:Image`
  Set Sim Data Type back to UInt8, then compress with “JPEG” of Quality 10
  Compression support (LZ4 and JPEG)!

## Slide 17: Image Compression

## Slide 18: Custom PV Data
SNS Beam Lines started to use this in ~2014
  cd /ics/examples/24_pvaccess ./start_neutrondemo -h ./start_neutrondemo -d 0.5 -r -m
  pvinfo neutrons pvmonitor neutrons
Allows fetching just what’s needed:
  # For detector pixel display pvget -r 'field(pixel)' neutrons pvmonitor -r 'field(timeStamp, pixel)' neutrons
  # For energy displays pvmonitor -r 'field(time_of_flight, pixel)' neutrons

## Slide 19: Custom PV Data in CS-Studio
Cannot handle arbitrary structure
  pva://neutrons
Can handle fields which are scalar or array
  pva://neutrons/proton_charge
  pva://neutrons/pixel
css –resource /ics/examples/24_pvaccess/PVA_Neutrons.bob

## Slide 20: History: Two compatible Implementations
Initial Implementation (Since ~2014)
  C++: pvDataCPP, pvAccessCPP, …
  Java: pvDataJava, pvAccessJava, …
  Python: pvaPy
  Gateway: pva2pva
Included in EPICS 7: softIocPVA, ‘QSRV’, pvget/put/info/monitor
Used in successful operation
Same API for C++ & Java: Lowest common denominator, missing language advantages.
Bugfixes, but no additions.
Updated Implementation (~2020)
  C++: PVXS
  Java: core-pva
  Python: p4p
  Gateway: p4p gateway
APIs take advantage of each language
Gateway’s “fair” scheduling helps with arrays; known UDP port allows use via firewalls
Active Development
  IPv6 support
  EPICS_PVA_NAME_SERVERS for TCP-only usage
Not in EPICS base, yet.
Same Protocol!

## Slide 21: PV Access and Python
Basic ‘get’, ‘put’, ‘monitor’
PV Access server for normative types or custom data
  See *.py examples under
  cd /ics/examples/24_pvaccess
  May have to use ‘python3’ since just ‘python’ is older version 2.x

## Slide 22: Custom PV Data from IOC Records
`makeBaseApp.pl –t example` includes “group”, see /ics/examples/07_customApp/Db/circle.db, /ics/examples/iocBoot/ioc_custom
  Calc records ..:circle:x & ..:circle:y compute (x, y) coordinate on circle
  info() annotations create PV ”training:circle” PV as struct { angle, x, y }
PVA “training:circle” updates atomically
  camonitor training:circle:x training:circle:y receives separate x, y updates pvmonitor training:circle will always see sqrt(x2+y2)==1
  cd /ics/examples/24_pvaccess python circle.py

## Slide 23: State of PV Access by late 2022
Done, operational
Server and client libraries for C++, Java, Python
  2nd version
Area Detector image transfer
  Used to distribute processing from camera hosts
Custom data servers and clients
  SNS: neutron data
  APS: services
Done, to be tested
PV server for records in IOC
  All record types
  ‘Description’
  Full ‘units’
  Full 64 bits for ‘int64in’, ‘int64out’
  No enum state limit
  Supports changing metadata
CS-Studio client
Gateway
To do
IOC links
  Default to CA. Initial support for field(INP, {pva:{pv:”tgt”}})
  Channel Access Get/put callback  ??
How to best combine data from records into custom PVA data?

## Slide 24: Summary: PV Access is ..
Alternative to Channel Access
  Both can be used in parallel
Similar, but supports custom data types
  Already useful for images and site-specific cases
Since EPICS 7 included in base IOC
  Details of ‘group’, ‘field(…)’ access still evolving