## Slide 1: PV Access Java API
EPICS Collaboration Meeting
Slovenia, Sept. 2022
Kay Kasemir

## Slide 2: History: Two compatible Implementations
Initial Implementation (Since ~2014)
  C++: pvDataCPP, pvAccessCPP, …
  Java: pvDataJava, pvAccessJava, …
  Python: pvaPy
  Gateway: pva2pva
Included in EPICS 7: softIocPVA, ‘QSRV’, pvget/put/info/monitor
Used in successful operation
Same API for C++ & Java: Lowest common denominator, missing language advantages.
Bugfixes, but no additions.
Updated Implementation (~2020)
  C++: PVXS
  Java: core-pva
  Python: p4p
  Gateway: p4p gateway
APIs take advantage of each language
Gateway’s “fair” scheduling helps with arrays; known UDP port allows use via firewalls
Active Development
  IPv6 support
  EPICS_PVA_NAME_SERVERS for TCP-only usage
Not in EPICS base, yet.
Same Protocol!

## Slide 3: `core-pva` Java Library
No dependencies beyond JRE
Source code:
  https://github.com/ControlSystemStudio/phoebus/tree/master/core/pva
  Builds with “mvn clean install” or “ant clean core-pva”
Releases:
  https://search.maven.org/search?q=core-pva
Sources are compatible with Java 8 for usage with Matlab, but you’ll have to compile with Java 8 yourself. Released binaries are for Java 11 or higher.
core-pva PVAClient & PVAChannel PVAServer & ServerPV
PVADouble, PVAString, PVAStructure, …
Java 8 or 11+ Runtime
Matlab
Your Code
core-pv Ref-counted pva://, ca://, sim:// .. PVs, VType mapping, RXJava value pipeline
CS-Studio Data Browser, Display Builder, Archive Engine, Alarm Server, …
PVWS Web Socket

## Slide 4: Examples
Source code: See src/test/…
Here we’ll use https://github.com/kasemir/JavaPVADemo
In VM terminal:
  cd /ics/examples/JavaPVADemo
  code .
.. and follow the README.MD

## Slide 5: Summary
`core-pva` is the current Java Client library
  CS-Studio
  Matlab (java8)
  Any Java code (java 11+ binaries are released)
Also includes simple PVA Server
  Mostly for tests at this time
Basic access to all PVA functionality

## Slide 7: pvDataJava & pvAccessJava vs. core-pva
Replaced large interfaces with “@FunctionalInterface”
Future<..the data..> instead of custom callback interfaces
Plain ‘instanceof’ instead of custom data API
PVADouble, PVAString, PVAStructure, … define a type and hold the data. Original implementation had twice the API because defining type was separate from holding data. In practice, all but the ‘pvinfo’ command needs type & data. Now ’info’ simply returns PVA… with values all zero/null/empty.