## Slide 1: Basic Linux Commands
Kay Kasemir
Jan. 2022

## Slide 2: Why Linux?
Control system devices tend to be different from desktop computers
  No monitor, no keyboard
  Only terminal access via network or serial
Remote access to control system servers is often also most efficient via terminal
EPICS “IOC” has no GUI because that would waste CPU & memory

## Slide 3: Getting around the file system
Change Directory
  cd /ics/examples/07_plc
  cd /iTAB/exTAB/07TAB
Show Current Directory (if not shown in terminal prompt)
  pwd
List files
  ls
  ls -l

## Slide 4: Dealing with Files
Open in Text Editor
  gedit name_of_file &
  gedit namTAB &
  may use vdct instead of gedit for EPICS database file
Quickly look at a file
  cat name_of_file
  less name_of_file (cursor up/down, ‘h’ for help)
Copy File
  cp name_of_file new_file_name
Remove/Delete file
  rm name_of_file

## Slide 5: Common EPICS Commands
Channel Access
  caget pv_name
  camonitor pv_name
  caput pv_name new_value
  cainfo pv_name
Start IOC
  softIoc –m “MACRO=value” –d example.db
  eipIoc –p plc=10.0.0.112 –m “MACRO=value” –d example.db
Start CS-Studio
  css

## Slide 6: Common IOC Commands
List Records
  dbl
Print fields of one record
  dbpr name_of_record 10
EtherIP Info
  drvEtherIP_dump
  drvEtherIP_report 10