## Slide 1: ‘makeBaseApp’ IOC
Kay Kasemir
Feb. 2022

## Slide 2: IOC binaries
softIoc
  Executes *.db files with ai, calc, …
softIocPVA
  Adds PVAccess server
eipIoc
  Understands ’field(DTYP, “EtherIP”)’
What if I want ‘myCustomIoc’ that includes PVA, EtherIP, Autosave, Stream Device, …?
“base”: ai, calc, …
Channel Access
“base”: ai, calc, …
Channel Access
PV Access
“base”: ai, calc, …
Channel Access
EtherIP
“base”: ai, calc, …
Channel Access
EtherIP
PV Access
Stream
“base”: ai, calc, …
Channel Access
AreaDetector
PV Access
Autosave
Autosave

## Slide 3: EPICS IOC
Channel Access, PVAccess
LAN
Sequencer
Device Support
I/O Hardware
IOC
Database
Database
  Records
  Remote access
  Access security
Sequencer
  C code for state machine
Device Support
  Include existing device support? Easy enough
  Have to write new device (driver) code? Varying degrees of difficulty

## Slide 4: softIoc, softIocPVA
IOC with Database engine, Channel Access, opt. PVA.
Comes with EPICS.
Need autosave, sequencer, device support?  Create your own IOC application binary!
Channel Access, PVAccess
LAN
IOC
Database

## Slide 5: ‘Host’ vs. ‘Target’ IOCs
Host-based, aka “soft” IOC
  Runs on same type of host (Linux, Mac, Windows) on which it’s compiled
  IOC is just another program on the host
  May run many IOCs on the same host
  Examples: `softIoc`, `softIocPVA`
Target IOC
  Cross-compiled from e.g. Linux to VxWorks
  Runs on VxWorks, RTEMS
  IOC is the primary, maybe only program running on the target
A lot of EPICS code can be used on both
  Records
  Device support for networked I/O

## Slide 6: How many custom IOC binaries?
Each IOC may use its own IOC binary
  More work?
  Allows updating binary for IOC 1 while IOCs 2-99 keep running
Or define common needs
  Vacuum IOC: Autosave, Support for AllenBradley PLC
  LLRF IOC: Autosave, Support for LLRF hardware
  Camera IOC: Autosave, AreaDetector
  Sample environment IOC: Autosave, Motor Record, Stream Device
… and update/restart all the vacuum IOCs together when changes are needed

## Slide 7: ‘makeBaseApp.pl’
Creates skeleton for custom IOC
  Directory structure
  Makefiles
  Examples: *.db, *.st, driver/device/record *.c
  IOC startup file
Two extremes
  makeBaseApp.pl –t example
    Get most everything; you delete what’s not needed
  makeBaseApp.pl –t ioc
    Just dirs & Makefiles; you add what’s needed

## Slide 8: EPICS Build Facility
Is outstanding
make, perl
Builds on Linux, Mac, Windows, for Linux, FreeBSD, OS X, Windows, vxWorks, RTEMS, x86, x86_64, ppc, arm, …
AppDevGuide
Functioned for decades across many changes of OSs, compilers, …
Is aggravating
Why is it not a Visual C++, Kdeveloper, VSCode, … project? What about CMake, GNU automake, … ?
What’s the name of that option again?
What’s causing this error now?

## Slide 9: ‘demo’ based on ‘example’ template
# Go somewhere mkdir –p /ics/mine cd /ics/mine
# Create IOC application of type ‘example’, # using ‘demo’ in the generated names makeBaseApp.pl -t example demo
# Create IOC startup settings of type ‘example’, # call it ‘demo’ because it’s for the app of that name makeBaseApp.pl -t example -i demo # When prompted, use the previously created ‘demo’ # application as the one that the IOC should load
# Compile everything make
# Start IOC cd iocBoot/iocdemo chmod +x st.cmd ./st.cmd
Repeat after changes

## Slide 10: Directory Layout: Key Files
To study the skeleton, check files before the first ‘make’ or after a ‘make distclean’
# makeBaseApp.pl -t example demo configure/RELEASE configure/CONFIG_SITE demoApp/Db/*.db demoApp/Db/*.substitutions demoApp/Db/Makefile demoApp/src/Makefile
# makeBaseApp.pl -t example -i demo iocBoot/iocdemo/Makefile iocBoot/iocdemo/st.cmd

## Slide 11: configure/RELEASE
Defines the path to EPICS base and other modules
  EPICS_BASE=/ics/tools/base-7.0.6
  SNCSEQ = /ics/tools/seq-2.2.9
  AUTOSAVE = /ics/tools/autosave-R5-10-2
Since about 3.15, includes ../RELEASE.local
  basedir/RELEASE.local: Lists all the modules
  basedir/top1/configure/RELEASE – includes ../../RELEASE.local basedir/top1/abcApp/ - uses EPICS base etc. basedir/top1/iocBoot/ - IOC bootups
  basedir/top2/configure/RELEASE – includes ../../RELEASE.local basedir/top2/xyzApp/ - uses EPICS base etc. basedir/top2/iocBoot/ - IOC bootups

## Slide 12: demoApp
xyzApp/Db Database files
xyzApp/src *Main.cpp, Sequences, custom device support, Makefile that lists required *.dbd and libs

## Slide 13: HowTo: Add Database files
Create xyzApp/Db/another.db
  For simple database, can test via softIoc –d another.db
Add to xyzApp/Db/Makefile:
  DB += another.db
make
  Now it’s under db/another.db
Add to iocBoot/iocwhatever/st.cmd
  dbLoadRecords "db/another.db", "macro=value”
(Re-)start the IOC

## Slide 14: Directory Layout: Generated Files
Beware of difference:
xyzApp/Db/*
  Database ‘Sources’. Edit these!
db/*
  ‘Installed’ databases, may have macros replaced. Will be overwritten by next ‘make’!
**/O.Common **/O.linux-x86_64 **/O.* db/* dbd/* include/* lib/* bin/*

## Slide 15: *.dbd: Database Descriptions
IOC record types, device support, … are extensible
  Implement new record type, new device support: Write C/C++ code for certain interfaces, compile.
  Then ‘register’ your addition with core IOC code: *.dbd file
Internals: VxWorks RTOS, the original IOC target, had runtime loader and symbol table. RTEMS, .. don’t necessarily offer this. EPICS build facility generates IOC startup source code from *.dbd file.

## Slide 16: HowTo: Add Support Modules (Device, …)
Example: ‘Autosave’
Define path in configure/RELEASE or better in ../RELEASE.local
  AUTOSAVE=/ics/tools/autosave-R5-10-2
Add binary and DBD info to xyzApp/Db/Makefile: YourProduct_DBD += asSupport.dbd YourProduct_LIBS += autosave
Use the support module in the IOC startup file: cd ${AUTOSAVE} dbLoadRecords "db/save_restoreStatus.db", "P=demo” set_requestfile_path("/home/controls/var") create_monitor_set(...)
Details on how to use a support module depend on the specific one, including names of provided *.dbd, binary, *.db, IOC commands

## Slide 17: Summary
makeBaseApp.pl creates the IOC skeleton
Good practice:
  Use makeBaseApp.pl –t example… for copy/paste.
  Create empty operational setup, and only paste-in what you need.
  Do it in small steps.
Much more: EPICS Application Developer’s Guide