## Slide 1: EPICS Database Updates
Kay Kasemir
Many slides from Andrew Johnson, APS/ANL
Jan. 2022

## Slide 2: Comparably New Database Features
Wildcards for ‘patch’ databases
Long Strings
JSON Notation for links and subscriptions

## Slide 3: ‘Patch’ Database
Database files can modify fields of existing records or add new fields/records
ps.db limit.db st.cmd
record(ai, “voltage”) { field(DTYP, … INP … field(SCAN, “2 second”) field(FLNK, ”current”) }
record(ai, “current”) { field(DTYP, … INP … field(FLNK, ”power”) } record(calc, “power”) { field(INPA, “voltage”) field(INPB, “current”) field(CALC, “A*B”) }
record(bo, “ps_enable”) …
record(ai, “voltage”) { field(SCAN, “.1 second”) } record(calc, “power”) { field(FLNK, “limit”) } record(calcout, ”limit”) { field(INPA, “power”) field(CALC, “A < 100”) field(OUT, “ps_enable”) }
dbLoadRecords “db/ps.db”
dbLoadRecords “db/limit.db”
May help to organize records.
“ps.db” can be used standalone, or with “limit.db”.
Order of loading *.db files matters!

## Slide 4: ‘Patch’ Database …
Note that the record type cannot be changed. Must know the type of record, or use “*” to patch any type
ps.db limit.db
record(ai, “voltage”) { field(DTYP, … INP … field(SCAN, “2 second”) field(FLNK, ”current”) }
record(ai, “current”) { field(DTYP, … INP … field(FLNK, ”power”) } record(calc, “power”) { field(INPA, “voltage”) field(INPB, “current”) field(CALC, “A*B”) }
record(bo, “ps_enable”) …
record(ai, “voltage”) { field(SCAN, “.1 second”) } record(“*”, “power”) { field(FLNK, “limit”) } record(calcout, ”limit”) { field(INPA, “power”) field(CALC, “A < 100”) field(OUT, “ps_enable”) }
In this example, the patch database doesn’t care if “power” is a calc, calcout, .. type of record
See /ics/examples/02_fishtank, tank.db is patched by control*db

## Slide 5: Long Strings
Unfortunately, EPICS ‘STRING’ was initially defined as CHAR[40]
Channel Access uses DBF_STRING = CHAR[40]
Record names, INP links can now be much longer
  field(INPA, "SomeReallyLongRecordNameThatExceeds40Characters PP MS")
..but you cannot read/modify them via channel access
See /ics/examples/12_long_strings, strings.db and display

## Slide 6: Old Workaround
Use record(waveform, ”long_string") { field(FTVL, "CHAR") field(NELM, "200") }
.. and (!) tell client that CHAR[] is not meant to be BYTE[] but long STRING. caget -S …., Format: String in operator interface tools
See /ics/examples/12_long_strings, strings.db and display

## Slide 7: New Workaround
IOC turns any string for VAL, INP, DOL into long-string CHAR[] if PV name ends in ‘$’
Long-String input and output records “lsi” and “lso” default to VAL of type STRING, but VAL$ becomes CHAR[]
Clients still need to be told if CHAR[] is BYTE[] or long string!
See /ics/examples/12_long_strings, strings.db and display

## Slide 8: JSON Notation for INP links
New support for JSON notation allows providing more detail
First practical use: {const:…}
  record(lsi, "lsi_init") { field(INP, {const:"Hello, this is a string and it can be really long!") field(PINI, "YES") } record(waveform, "array") { field(FTVL, "CHAR") field(NELM, "200") field(INP, {const:[65, 66, 67, 68, 69]) field(PINI, "YES") }
See /ics/examples/12_long_strings/strings.db

## Slide 9: JSON: “JavaScript Object Notation”
Standard text representation of data
  Can represent “anything”
  More compact than e.g. XML
EPICS starts to use it to provide details for
  Links, see https://epics.anl.gov/base/R7-0/6-docs/links.html
  Subscriptions, see https://epics.anl.gov/base/R7-0/6-docs/filters.html
  .. More to come
{ number: 3.14, text: "Hello!", substructure: { numbers: [1, 2, 3, 4] } }

## Slide 10: JSON Notation for Subscription Filters
In one window, run
  cd /ics/examples/01_first_steps softIoc –d ramp1.db
In other window, compare the following camonitor limit camonitor 'limit.{ts:{}}’
  camonitor ramp camonitor 'ramp.{dbnd:{abs:1.9}}'