## Slide 1: Area Detector
Feb. 2022
Kay Kasemir, Klemen Vodopivec based on presentations by Mark Rivers, APS, U. Chicago

## Slide 2: Area Detector
EPICS framework for image manipulation
Cameras
  Cheap “Web Cam”
  $$$ high speed, high res.
  Neutron, X-Ray detectors
Plugins collection
  ROI
  Transform
  ColorConvert
  Etc.
Extendibility

## Slide 3: Features
Maybe the largest shared EPICS Application
PVs for image settings, shutter, exposure, …
  “Simulated” area detector IOC has 6000 records
N-D data
  1D: time series data
  2D: images (most common)
  N<=10
  Custom metadata
Supports >500 frame/second detectors

## Slide 4: Disclaimer
This will only scratch the surface.
EPICS web site has several days of training material if you are serious about using the A.D.

## Slide 5: Vocabulary
NDArray
  Structure holding data
  N-dimensional array
    N=2 for basic greyscale image
    N>2 for color, detector with “depth”
NDAttribute
  Metadata attached to NDArray
    Motor position, temperature, shutter,…
  Added by driver, from PVs, Plugins…
NDArrayPool
  Pool of NDArrays to reduce memory allocation
Driver
  Interface to camera
  Vendor libraries, custom protocols
  Creates NDArray
Plugin
  Manipulates NDArray data
  May change data
  May send data to other plugins
    No-copy if not changed

## Slide 6: EPICS AreaDetector Architecture

## Slide 7: Configurable plugins mechanism
Camera Driver
Transform (rot90)
Scatter
FFT
FFT
Gather
Stats
File
Legend:
CPU1
CPU2
CPU3
CPU4
--- original data
--- modified data
Stats
Reads images from camera
Rotates images 90deg clockwise
Provides PVs like min, max intensity
Splits series of images into two channels equally
Merges into single channel
CPU intensive operation

## Slide 8: Using ‘ADSimDetector’
Start IOC
  cd /ics/examples/AreaDetector ./start_sim_ioc.sh
Open Display
  ﻿css -resource /ics/examples/AreaDetector/AreaDetectorDemo.bob
Select “Start” and “Enable”

## Slide 9: ADSimDetector
Open the “Detector” Page
Under “Collect”, set the “Acquire Period” to 0.5
Observe counter for images and rate on main page

## Slide 10: NDPluginStdArrays
Serves image as Channel Access waveform
On Detector, Plugins, All, find NDPluginStdArrays
  Port = “SIM1”
  Enable
AreaDetectorDemo.bob shows image
  PV: 13SIM1:image1:ArrayData
  Data Width x Height: 1024 x 1024
  [x] Unsigned

## Slide 11: NDPluginOverlay
Adds rectangles, text etc. to image
On Detector, Plugins, All, find NDPluginOverlay “OVER1”
  Set its Port to “SIM1”, Enable
  Change NDPluginStdArrays’s Port to “OVER1”
  Press “More”, select first of the “Individual Overlays”

## Slide 12: NDPluginOverlay.. Overlay #1
Configure as shown:

## Slide 13: What we did
Area Detector IOC
SIM1
OVER1
Image1
Driver
Plugins
OVER1 offers 8 overlays:
Rectangle
Text “Hello”
…

## Slide 14: NDPluginStats
Computes min, max intensity etc.
Computes profiles
Advanced image statistics
  Excess Kurtosis (flatness)
  Skewness (symmetry)
  Centroid & sigma
On Detector, Plugins, All, find NDPluginStats “STATS1”, “More”
  Set its Port to “SIM1”, Enable
  Note how the Statistics show min..max of 0..255

## Slide 15: NDPluginROI
Performs Region-Of-Interest calculations
  Selects part of image
On Detector, Plugins, All, find NDPluginROI “ROI1”, “More”
  Set its Port to “SIM1”, Enable
  Set X and Y ROI size to 10, so ROI is small 10x10 corner of image
Back in STAT1, change port from “SIM1” to “ROI1”
  Note how the Statistics show a varying min..max as the image data rolls through that ROI

## Slide 16: What we did
Area Detector IOC
SIM1
OVER1
Image1
Driver
Plugins
STATS1
ROI1

## Slide 17: More Plugins
Process
  Background subtraction, clipping, recursive averaging over N images, ..
Saving images in various formats
  Adding data from PVs as “Attributes”
  PNG, JPEG, TIFF, HDF5, …
Serving NDArray via PVA
  For displays: No need to configure size, data type, …
  For ADPvAccess Driver: Process data on different hosts

## Slide 18: NDPluginPVA – Serve PVA ‘Image’
In Plugins, “PVA1”
  Set its Port to “SIM1” or “OVER1”, Enable
PVAccess Tests
  pvlist
  pvinfo 13SIM1:Pva1:Image
  pvget -r 'field(dimension)' 13SIM1:Pva1:Image
In Display
  Use “Image” widget
  Set PV
  No need to configure data size, data type

## Slide 19: NDPluginPVA – Serve PVA ‘Image’
Display adapts when image size and data type change

## Slide 20: Area Detector
Ecosystem for handling
Cameras
Detectors
“Images” in EPICS