## Slide 1: Python Channel Access Clients
Kay Kasemir
Feb. 2022

## Slide 2: Channel Access Operations
‘connect’
‘get’, ‘get-callback’, ‘monitor’
‘put’, ‘put-callback’
‘disconnect’

## Slide 3: ‘connect’
Based on channel name, UDP search, ..
  See earlier Channel Access overview
Connection might take a few seconds
Network interruptions do happen
  CA client libraries will automatically re-connect
  API for being notified about connect/reconnect

## Slide 4: ‘disconnect’
A long-running program might
  Connect PVs ”A”, “B”, “C”, use them for a while, disconnect
  Connect PVs ”X”, “Y”, “Z”, use them for a while, disconnect
  Cleanup resources on the CA server/IOC, reduce network traffic
Quick and dirty script may just connect, use, quit

## Slide 5: ‘get’, ‘get-callback’, ‘monitor’ - read, subscribe
‘get’
  Request value
  Wait for value (with timeout of ~ seconds)
‘get-callback’
  Request value
  Callback invoked once as value arrives
‘monitor’
  Register for updates
  Callback invoked whenever a value arrives, until monitor cancelled

## Slide 6: ‘put’, ‘put-callback’ - write
‘put’
  Send a value
  Error in case channel not connected right now, or no write access. Otherwise done.
‘put-callback’
  Send a value
  Callback invoked once the value has been received by CA server and ‘completed’. For PV related to motor record on IOC, this can mean motor drive has been energized, motor moved to appropriate target location, then performed N adjustments to perfectly reach the desired position, and finally motor drive was de-energized.

## Slide 7: Higher Level CA Client Bindings
Cached PVs
  When first asked for a channel, some PV object is created which connects and tracks connection state.
  When your program later asks for the same PV, it gets that cached PV which is already connected
Subscribed
  PV always monitors. If you read the value of a PV, you get the most recent monitor right away
Write
  Writing a PV tends to be the plain ‘put’, a fire-and-forget that doesn’t delay your program and will eventually reach the CA server/IOC
 Convenient and performant for most clients

## Slide 8: Python Example

## Slide 9: Automation: This doesn’t cut it
write 10 to ”motor:setpoint” read detector data
save data in file for “position10”
Your motor might still be moving while you take data

## Slide 10: Automation: Not ideal, either
write 10 to ”motor:setpoint” while abs(read(“motor:position”) – 10) < 0.1: sleep 1 second
# OK, we’re at the desired position read detector data
save data in file for “position10”
Maybe, maybe not

## Slide 11: Automation: How do you know you’re “done”?
Time
Temp, pos, …
Setpoint
Readback
done?
done?
done!

## Slide 12: Automation: Use ’put-callback’
Only logic on IOC really knows when it’s done
  Motor record: Performed initial backlash-compensated move, then retries, now motor is at rest and we’re “done”
  Lakeshore controller: Calc records, busy record, sequence knows when it’s “done”
With ‘put-callback’, IOC will tell you when it’s “done”
Alas, no way to tell from the outside if a PV supports put-callback. If not, put-callback returns right away even though the device is not “done”.

## Slide 13: Automation: Use explicit ‘get’, ‘get-callback’
In a higher level library, ‘PV.read()’ might only tell you about the last received monitor. The actual record might have a new value that you will soon receive via a monitor, but unclear when exactly. Based on MDEL, you might never get the exact value.
Explicit ‘get’ or ‘get-callback’ will force a round-trip read/response, fetching the most recent value.

## Slide 14: Another Python Example

## Slide 15: Yet Another Python Example
More: https://github.com/pyepics/pyepics

## Slide 16: Other CA Client Options
Python ‘PVA’ client for the new PVAccess Protocol
Matlab/Octave/Scilab MCA resp. LabCA bindings
SNL/Sequencer
Display Builder scripts
Plain C code calling CA.lib
Plain Java code calling JCA.jar

## Slide 17: Summary
Higher level bindings like python are pretty easy:
  caget, caput
For dependable automation, remember get/put-callback
  .. and use IOC that supports it