## Slide 1: ‘makeBaseApp’ IOC
Kay Kasemir
July 2026

## Slide 2: IOC binaries
softIoc
  Executes *.db files with ai, calc, …
softIocPVA, softIocPVX
  Adds PVAccess server
What if I want ‘myCustomIoc’ that includes PVA, EtherIP, Autosave, Stream Device, …?
“base”: ai, calc, …
Channel Access
“base”: ai, calc, …
Channel Access
PV Access
“base”: ai, calc, …
Channel Access
EtherIP
PV Access
Stream
“base”: ai, calc, …
Channel Access
AreaDetector
PV Access
Autosave
Autosave
eipIoc
  Adds EtherIP
“base”: ai, calc, …
Channel Access
EtherIP

## Slide 3: ‘Soft IOC’, ‘Real IOC’, ‘Host’, ‘Target’
Host-based, aka “soft” IOC
  Runs on same type of host (Linux, Mac, Windows) on which it’s compiled
  IOC is just another program on the host
  May run many IOCs on the same host
  Examples: `softIoc`, `softIocPVA`, all IOCs in this training session
Target IOC
  Cross-compiled from e.g. Linux to VxWorks, RTEMS, embedded Linux
  Runs on VME, µTCA, embedded CPU
  IOC is the primary, maybe only program running on the target
  IOCs on VxWorks, talking to VME hardware, were the original IOCs
A lot of EPICS code can be used on both
  Records
  Device support for networked I/O

## Slide 4: ‘makeBaseApp.pl’
Creates skeleton for custom IOC
  Directory structure
  Makefiles
  Examples: *.db, *.st, driver/device/record *.c
  IOC startup file
Two extremes
  makeBaseApp.pl –t example
    Get most everything; you delete what’s not needed
  makeBaseApp.pl –t ioc
    Just dirs & Makefiles; you add what’s needed

## Slide 5: EPICS Build Facility
Is outstanding
Builds on Linux, Mac, Windows, for Linux, FreeBSD, OS X, Windows, vxWorks, RTEMS, x86, x86_64, ppc, arm, …
AppDevGuide
Served us for decades across many changes of OSs, compilers, …
Is aggravating
Why is it not a Visual C++, Kdeveloper, VSCode, … project? What about CMake, GNU automake, … ?
What’s the name of that option again?
What’s causing this error now?

## Slide 6: ‘demo’ based on ‘example’ skeleton
rm –rf /ics/examples/mine mkdir –p /ics/examples/mine cd /ics/examples/mine
# Create IOC application of type ‘example’, # using ‘demo’ in the generated names makeBaseApp.pl -t example demo
# Create IOC startup settings of type ‘example’, # call it ‘demo’ because it’s for the app of that name makeBaseApp.pl -t example -i demo # When prompted, use the previously created ‘demo’ # application as the one that the IOC should load
# Compile everything make
# Start IOC cd iocBoot/iocdemo chmod +x st.cmd ./st.cmd
Repeat after changes

## Slide 7: Directory Layout: Key Files
To study the skeleton, check files before the first ‘make’ or after a ‘make distclean’
# makeBaseApp.pl -t example demo configure/RELEASE configure/CONFIG_SITE demoApp/Db/*.db demoApp/Db/*.substitutions demoApp/Db/Makefile demoApp/src/Makefile
# makeBaseApp.pl -t example -i demo iocBoot/iocdemo/Makefile iocBoot/iocdemo/st.cmd

## Slide 8: configure/RELEASE
Defines the path to EPICS base and other modules
  EPICS_BASE﻿=/ics/tools/base
  SNCSEQ =/ics/tools/sequencer
  AUTOSAVE =/ics/tools/autosave
Since about version 3.15, includes ../RELEASE.local
  basedir/RELEASE.local: Lists all the modules
  basedir/top1/configure/RELEASE – includes ../../RELEASE.local basedir/top1/abcApp/ - uses EPICS base etc. basedir/top1/iocBoot/ - IOC bootups
  basedir/top2/configure/RELEASE – includes ../../RELEASE.local basedir/top2/xyzApp/ - uses EPICS base etc. basedir/top2/iocBoot/ - IOC bootups

## Slide 9: demoApp
xyzApp/Db Database files
xyzApp/src *Main.cpp, Sequences, custom device support, Makefile that lists required *.dbd and libs

## Slide 10: Start over: ‘demo’ based on ‘ioc’ skeleton
rm –rf /ics/examples/mine mkdir –p /ics/examples/mine cd /ics/examples/mine
# Create IOC application of type ‘ioc’, # using ‘demo’ in the generated names makeBaseApp.pl -t ioc demo
# Create IOC startup settings of type ‘ioc’, # call it ‘demo’ because it’s for the app of that name makeBaseApp.pl -t ioc -i demo # When prompted, use the previously created ‘demo’ # application as the one that the IOC should load
# Compile everything make
# Start IOC cd iocBoot/iocdemo chmod +x st.cmd ./st.cmd
Repeat after changes
 Empty IOC!

## Slide 11: How To Add Database Files
Create demoApp/Db/another.db
  For simple database, can test via softIoc –m "macro=value" –d another.db
Add to demoApp/Db/Makefile:
  DB += another.db
make
  Now it’s under db/another.db
Add to iocBoot/iocdemo/st.cmd
  dbLoadRecords "db/another.db", "macro=value”
(Re-)start the IOC

## Slide 12: Directory Layout: Generated Files
Beware of difference:
xyzApp/Db/*
  Database ‘Sources’. Edit these!
db/*
  ‘Installed’ databases, may have macros replaced. Will be overwritten by next ‘make’!
**/O.Common **/O.linux-x86_64 **/O.* db/* dbd/* include/* lib/* bin/*

## Slide 13: Plain Database files, Macros, Templates
# demoApp/Db/plain.db
record(calc, "noise")
{
field(SCAN, "1 second")
field(CALC, "RNDM*10")
}
﻿# demoApp/Db/Makefile
…
DB += plain.db
# db/plain.db
record(calc, "noise")
{
field(SCAN, "1 second")
field(CALC, "RNDM*10")
}
# iocBoot/iocdemo/st.cmd
…
﻿dbLoadRecords("../../db/plain.db")
‘make’
# IOC shell ﻿epics> dbl
noise
Open 3 terminals:
For running ‘make’: cd /ics/examples/05_template
For editing database files: cd /ics/examples/05_template/demoApp/Db
For running ./st.cmd cd /ics/examples/05_template/iocBoot/iocdemo

## Slide 14: Plain Database files, Macros, Templates
﻿# demoApp/Db/macro.db
record(calc, "noise$(NUM)")
{
field(SCAN, "1 second")
field(CALC, "RNDM*$(LIMIT)")
}
﻿# demoApp/Db/Makefile
…
DB += macro.db
# db/macro.db
record(calc, "noise$(NUM)")
{
field(SCAN, "1 second")
field(CALC, "RNDM*$(LIMIT)")
}
# iocBoot/iocdemo/st.cmd
…
﻿dbLoadRecords("../../db/macro.db","NUM=1,LIMIT=10")
dbLoadRecords("../../db/macro.db","NUM=2,LIMIT=100")
‘make’
# IOC shell ﻿epics> dbl
noise1
noise2
﻿epics> dbgf noise2.CALC
DBF_STRING: "RNDM*100"

## Slide 15: Plain Database files, Macros, Templates
﻿# demoApp/Db/macro.db
record(calc, "noise$(NUM)")
{
field(SCAN, "1 second")
field(CALC, "RNDM*$(LIMIT)")
}
﻿# demoApp/Db/Makefile
… # macros.db will be created # from macros.substitutions!
DB += macros.db
# db/macros.db
record(calc, "noise1")
﻿{
field(SCAN, "1 second")
field(CALC, "RNDM*10")
}
record(calc, "noise2")…
record(calc, "noise3")…
record(calc, "noise4")…
# iocBoot/iocdemo/st.cmd
…
﻿dbLoadRecords("../../db/macros.db”)
‘make’
# IOC shell ﻿epics> dbl
noise1
noise2
noise3
noise4
﻿epics> dbgf noise4.CALC
DBF_STRING: "RNDM*400"
﻿# demoApp/Db/macros.substitutions
﻿file "macro.db"
{
{ NUM="1", LIMIT="10" }
{ NUM="2", LIMIT="100" }
}
﻿file "macro.db"
{
pattern { NUM, LIMIT }
{ 3, 300 }
{ 4, 400 }
}
Original syntax
Alternate syntax
“Template”
Expanded
Template

## Slide 16: Plain Database files, Macros, Templates?
Plain database files?
  Add at least some naming macro like record(xx, “$(P):Motor”) to allow running with P=Test or P=ActualGadget
Macros in *.db
  Whenever there’s more than one instance of something, macros make sense
  Perfectly fine to load them with ﻿dbLoadRecords(”file_with_macro.db",”P=ABC,NUM=1")
Template/Substitutions?
  Some prefer *.substitutions, expanded by ‘make’, over expanding macros in dbLoadRecords because file on disk then holds all the expanded record names. fgrep noise1 db/* will find that record in expanded file

## Slide 17: *.dbd: Database Descriptions
IOC record types, device support, … are extensible
  Implement new record type, new device support: Write C/C++ code for certain interfaces, compile.
  Then ‘register’ your addition with core IOC code: *.dbd file
Internals: VxWorks RTOS, the original IOC target, had runtime loader and symbol table. RTEMS, .. don’t necessarily offer this. EPICS build facility generates IOC startup source code from *.dbd file.

## Slide 18: How To Add Support Modules (Device, …)
Example: ‘Autosave’
Define path in configure/RELEASE or better in ../RELEASE.local
  AUTOSAVE=/ics/tools/autosave
Add binary and DBD info to xyzApp/src/Makefile: YourProduct_DBD += asSupport.dbd YourProduct_LIBS += autosave
Use the support module in the IOC startup file: cd ${AUTOSAVE} dbLoadRecords "db/save_restoreStatus.db", "P=demo” set_requestfile_path("$(TOP)/iocBoot/$(IOC)/autosave") create_monitor_set(...)
Details on how to use a support module depend on the specific one, including names of provided *.dbd, binary, *.db, IOC commands

## Slide 19: Site specifics
Most EPICS sites use a makeBaseApp layout at the core
  Local expert understands the details
  Everybody else uses existing setups to add/modify database files
Many sites wrap with local tool to
  Create new IOC setups
  Start/stop IOCs as ‘procServ’ Linux services with console access & log
$ ioc create --engineer "Ozzy Osbourne” --location "8600 J-105” --host "ics-srv-softioc1” -m "autosave=R5-11, StreamDevice=2.8.26” ics-ioc-xxx`

## Slide 20: Summary
makeBaseApp.pl provides the commonly used IOC skeleton
You need some minimal understanding
Work in xxxApp/Db/, not db/
make
IOC runs iocBoot/iocXXX/st.cmd