## Slide 1: CA/PVA Channel vs. IOC Record vs. other CA/PVA server
Kay Kasemir
July 2026

## Slide 2: What is a Process Variable (Channel)?
Good question!
"A named piece of data with properties”

## Slide 3: What is a PV (Channel)?
Whenever there's a CA/PVA server out there which decides to respond to a search request, that's a PV!
IOC responds to "{record}.{field}" searches if
  {record} names a record on this IOC,
  {field} is an accessible field of that record (using VAL if no .{field} given),
  or it's the pseudo-field "RTYP" (record type).
  Every field of every record is a PV!
When you implement your own server based on the CAS/PVA library (C++, python, …), you decide when to respond!

## Slide 4: Channel Properties
For CA, DBR_... request types are fixed:
    DBR_DOUBLE, DBR_SHORT, …: Just value.
    DBR_STS_...: Value with status and severity.
    DBR_TIME_...:Value with status, severity and time stamp.
    DBR_CTRL_...:Value, status, severity, units, limits, … but NOT time
  Not available:
    Custom combinations like value with units.
  See `caget –h`
For PVA, “Normative Types” offer same info as all DBR_... types combined
  See separate PVA presentation

## Slide 5: Records & Fields vs. Channels & Properties
A CA/PVA client asks for a channel with properties
The implementer of the server decides how to answer.
  The IOC maps the fields of a record to the properties of a channel.
  Details are ultimately in the IOC source code

## Slide 6: How do records & fields map to channels & properties?
Analog Record (ai, calc, …)
Fields
  VAL
  DESC
  EGU
  PREC
  LOPR, HOPR
  LOLO, LOW, HIGH, HIHI
  TIME
Channel
DBR_CTRL_DOUBLE
  value
  status/severity
  time stamp*
  units
  precision
  display limits
  warn limits
  alarm limits
  ctrl limits
?
* Actually, DBR_CTRL does not include time stamp. But DBR_TIME would.

## Slide 7: Consider this Record
record(calc, "t1:calcExample") { field(DESC, "Sawtooth Ramp") field(SCAN, "1 second") field(CALC, "(A<10)?(A+1):0") field(INPA, "t1:calcExample.VAL") field(PREC, "2") field(EGU, ”steps") field(LOPR, "0") field(HOPR, "10") field(HIGH, "8") field(HIHI, "9") }
t1:calcExample as DBR_CTRL_DOUBLE
  value = VAL
  status/severity = STAT/SEVR
  units = EGU
  precision = PREC
  display limits = LOPR/HOPR
  warn limits = LOW/HIGH
  alarm limits = LOLO/HIHI
  ctrl limits = LOPR/HOPR
t1:calcExample.DESC as DBR_TIME_STRING
  value = DESC
  status/severity = STAT/SEVR
  time stamp = TIME
t1:calcExample.SCAN as DBR_CTRL_ENUM
  value = SCAN
  status/severity = STAT/SEVR
  labels = [ “Passive”, .., “10 second”, .., “.1 second”]
t1:calcExample as DBR_TIME_DOUBLE
  value = VAL
  status/severity = STAT/SEVR
  time stamp = TIME
Makes sense!
Makes sense!
Alarm, time don’t apply to DESC!

## Slide 8: Consider a ‘news’ website…
People create web pages with news
http:// serves them
  Doesn’t mean you can list all the people, or get the color of their socks
  People might change
  Some pages are created by programs, they don’t wear socks!
Records on IOCs provide data
CA/PVA serves it
  Doesn’t mean you can list all records
  IOCs might change
  Some channels are provided by python, LabVIEW, …, there are no records!

## Slide 9: Keep in mind
The protocol http:// is different from the people who create web sites
The CA/PV protocol is different from the IOCs and records
This ‘decoupling’ has proven essential but is often forgotten !

## Slide 10: Key Points
Channel != Record
  IOC maps fields of records to properties of channel
  This separation allowed development of generic clients (displays, alarm tools, archives) independent from IOCs
There is a growing number of non-IOC CA/PVA servers
  Mostly python
  They provide channels “x” with value, units, precision, alarms, time.. but that doesn’t mean you can read/write “x.EGU”, “x.PREC”, … There is no record!
PVAccess allows custom data types
  But to remain compatible, try to support the Normative Types