## Slide 1: Archive
July 2026
Kay Kasemir

## Slide 2: End-User View of Archive
Databrowser can show history
  Easy, “Scroll back” on time axis
May access history from Python, Java, … to perform your own analysis
  Write a program to do that

## Slide 3: Basic Technical View of Archive
Archiver
  Reads PVs via Channel- or PVAccess
  Writes samples to Storage
  Provides history from Storage
IOC
CA Server
PVA Server
Archiver
Storage

## Slide 4: More Detail
Storage Theory: Tons of fast storage Practice: Slow, limited space
Archive Engine (Service)
Read PVs, write samples to storage
CA, PVA
Configuration:
Which channels? How?
IOC

## Slide 5: Choices…
 | Channel Archiver | Relational Database | TimescaleDB | EPICS Archiver Applicance
Storage | Custom “data” and “index” files | MySQL, Postgres, Oracle | Postgres optimized for time series | Custom
Storage Speed | Fast | Slow | Better than Slow | Fast
Storage Maintainability | Eventually impossible | Trivial (for RDB admin) | Trivial (for RDB admin) | A few files per channel
Configuration | XML file | RDB with XML file import/export | RDB with XML file import/export | Web interface, XML file import/export
Readout | DataBrowser, custom C++ lib | DataBrowser, any RDB client | DataBrowser, any RDB client | DataBrowser, web interface, web service

## Slide 6: Archiver Appliance Detail
Storage: Files with “Protobuf”-encoded samples
  One file per Channel and Stage
Example Stages:
  RAM disk for ”today”
  Solid-state disk for “this month”
  NFS-mounted folder for “older”
May create cluster of applicances
Web interface to add channels, monitor performance, fetch data
See https://epicsarchiver.readthedocs.io/en/stable for “Quickstart” and more

## Slide 7: Relational Database Detail
Storage: MySQL, Postgres, Oracle
  Ideal if you can leverage existing RDB cluster and admin support
  RDBs have been reliable for decades
Archive Engine, run as Linux service, writes samples to RDB
  May run one for “Vacuum”, one for “Cryogenics”, one for “Beamlines” etc.
Data accessible by Data Browser and pretty much any programming language
See https://github.com/ControlSystemStudio/phoebus/blob/master/services/archive-engine/doc/index.rst

## Slide 8: TimescaleDB Detail
RDB Admins may develop site-specific ways to “partition” the data and provide stored procedures for optimized data readout
TimescaleDB = Postgres with extensions to automatically partition time series data
https://github.com/ControlSystemStudio/phoebus/blob/master/app/databrowser-timescale/README.md

## Slide 9: Decisions…
Archiver appliance
  Safe option, used by many in EPICS community
  You’ll need somebody to maintain the data
RDB
  Very dependable, ideal if you already have RDB admin support and want to access the data in various ways
TimescaleDB
  New, no operational experience
  Promising option for new RDB setup, headstart over site-specific partitioning solutions

## Slide 10: IOC Configuration
Archive engines subscribe to “archive” aka “log” events (DBE_ARCHIVE)
  camonitor –m l the_pv_name
For analog records, configure the ADEL field*
  Unfortunately, not perfect for data with logarithmic behavior like vacuum pressures.
Assert that your IOC knows the time
  Check time stamps reported by camonitor
* Also: EGU, PREC, ZNAM, ONAM, … If it’s worth archiving, it should be properly configured.

## Slide 11: Archive Engine Options
Monitor
  Tries to save every received update
  Based on ADEL
  Might need an expected-update-period to allocate buffers, skipping samples if there are too many
Scan
  Writes the most recent value every N seconds
  Stores original time stamps

## Slide 12: Viewing Archived Data
Open Data Browser, add PV, zoom/pan/set time range
Relies on Data Browser Preferences:
org.csstudio.trends.databrowser3/urls=jdbc:mysql://localhost/archive|RDB org.csstudio.trends.databrowser3/archives=jdbc:mysql://localhost/archive|RDB org.csstudio.trends.databrowser3/use_default_archives=true﻿ org.phoebus.archive.reader.rdb/user=report org.phoebus.archive.reader.rdb/password=$report

## Slide 13: Archive
Fundamentally simple: Store values of PVs
There is no perfect implementation
  Can’t store everything at high rate forever
On IOC side, configure ADEL (and EGU, PREC, ZNAM, ONAM)
Looking at data in Data Browser is easy

## Slide 14
RDB example in training setup

## Slide 15: Initial RDB Archive Installation
See https://github.com/ControlSystemStudio/phoebus/blob/master/services/archive-engine/doc/index.rst
Install MySQL or MariaDB, PostgreSQL, Oracle
Setup archive tables
Check that this happened:
sudo systemctl start mariadb.service sudo systemctl status mariadb.service archive-engine -list

## Slide 16: Fishtank Example
Run IOC
  cd /ics/examples/fishtank ./st.cmd
In CS-Studio, open /ics/examples/fishtank/heater.bob  Current data
Right-click on plot, “Open Data Browser”
  Right-click to Show Toolbar
  Change time range  Archived data!

## Slide 17: Example archive for ‘fishtank’
cd /ics/examples/14_archive/
archive-engine -help
archive-engine –list
cat fishtank.xml
Import configuration and start sample engine:
archive-engine -engine fishtank -import `pwd`/fishtank.xml -replace_engine
archive-engine -engine fishtank
Check http://localhost:4812 in web browser
lynx –dump http://localhost:4812/main lynx –dump http://localhost:4812/stop

## Slide 18: If there is no archive setup: Data Browser
Run data browser as usual
Export “Plot” data
File looks just like data exported from archive
.. Workaround to capture a few hours of data, maybe over night

## Slide 19: If there is no archive setup: camonitor
Capture output of camonitor
$ camonitor epics-dev:tank | tee example.log epics-dev:tank 2026-06-09 13:04:33.782281 39.1624 epics-dev:tank 2026-06-09 13:04:34.282304 39.0474 …
Show with for example Gnuplot. (sudo dnf install gnuplot)