## Slide 1: PV Access
July 2026
Kay Kasemir

## Slide 2: EPICS Network Protocols
Channel Access
  Since beginning of EPICS
  DBR_*: Number, enum, string, scalar or array, with time, alarm, limits
  Still fully supported with bug fixes
PV Access
  Started as “EPICS V4”, since EPICS 7 (2017) in base
  PV Data: Arbitrary structures
  New features being added

## Slide 3: First Glance
softIocPVA instead of softIoc
  # We did this before: cd /ics/examples/fishtank cat st.cmd # Compare, then run: cd /ics/examples/15_pvaccess cat st.cmd ./st.cmd
pv… instead of ca…
  camonitor epics-dev:setpoint epics-dev:tank pvmonitor epics-dev:setpoint epics-dev:tank pvput epics-dev:setpoint 40 caput epics-dev:setpoint 30
CS-Stud﻿io:
  css -resource /ics/examples/15_pvaccess/pva.bob

## Slide 4: PV Access
Like Channel Access
  Name search via UDP
  Connection for data transfer via TCP
  EPICS_PVA_ADDR_LIST, EPICS_PVA_AUTO_ADDR_LIST
Get, put, monitor
  Plus an ‘RPC’ type operation
Arbitrary PV Data structures instead of DBR_.. types

## Slide 5: Custom Data: Great, but then what?
Fred’s structure: double value short status short severity string units time timeStamp …
Keith’s structure: short level double data string type time stamp …
Jane’s structure: short info double content string meta long ms …
Which number to show on a user display?
What units?
Is this an alarm?
Time stamp?
Jürgen’s structure: short grad double wert string typ long zeit …

## Slide 6: “Normative Types”
Channel Access
struct dbr_ctrl_double: short status short severity short precision char units[8] … no timestamp … double value struct dbr_time_double: short status short severity timestamp stamp double value
You get what you request (network always transfers complete struct)
PV Access
epics:nt/NTScalar: double value int alarm/status int alarm/severity string display/units int display/precision time timeStamp …
You get what you request (but network only transfers changes)

## Slide 7: Channel Access vs. PV Access
Similar command line tools:
caget epics-dev:tank
camonitor epics-dev:tank
cainfo epics-dev:tank
caget –d CTRL_DOUBLE epics-dev:tank # Not supported camonitor –d CTRL_DOUBLE epics-dev:tank
caget epics-dev:tank.SCAN
pvget epics-dev:tank
pvmonitor epics-dev:tank
pvinfo epics-dev:tank pvget –M raw epics-dev:tank
# Note first few updates! pvmonitor –M raw epics-dev:tank
pvget epics-dev:tank.SCAN
… and pvxget, pvxinfo, …

## Slide 8: CS-Studio
Use pva://… prefix to select PV Access
Use ca://… prefix to select Channel Access
Set default in ﻿/ics/tools/css_training.ini

## Slide 9: So it’s very similar, maybe more efficient…
What’s really new?
How about those custom structures?

## Slide 10: Images: Normative type NTNDArray
See Area Detector (NDPluginPVA) or cd /ics/examples/15_pv_access ./start_imagedemo
Terminal
pvinfo IMAGE
CS-Studio: Image widget
  Only needs pva://IMAGE
  See examples/15_pvaccess/ PVA_IMAGE.bob

## Slide 11: SNS Neutron Data
neutron
Sample
Detector
1) Where was the detector hit?
2) When was the detector hit? .. relative to start of cycle: 60 Hz, 30 Hz, … “Time of Flight”  Speed of neutron  Wavelength
3) Where & wavelength?
 Distance of scattering centers  Model of sample structure
scattered neutron
NaCl?
Diamond?

## Slide 12: Custom PV Data
SNS Beam Lines started to use this in ~2014
  cd /ics/examples/15_pvaccess ./start_neutrondemo
  pvinfo neutrons pvmonitor neutrons
Allows fetching just what’s needed:
  # For detector pixel display pvget -r 'field(pixel)' neutrons # For time of flight display pvmonitor -r 'field(timeStamp, pixel)' neutrons
  # For d-space displays pvmonitor -r 'field(time_of_flight, pixel)' neutrons
Detector
PVA neutron data
Processing IOC

## Slide 13: Custom PV Data in CS-Studio
Cannot handle arbitrary structure
  pva://neutrons
Can handle fields which are scalar or array
  pva://neutrons/proton_charge
  pva://neutrons/pixel

## Slide 14: PV Access and Python
Basic ‘get’, ‘put’, ‘monitor’
PV Access server for normative types or custom data
  See *.py examples under
  cd /ics/examples/15_pvaccess

## Slide 15: Custom PV Data from IOC Records
`makeBaseApp.pl –t example` includes “group”: rm –rf /ics/examples/mine mkdir –p /ics/examples/mine cd /ics/examples/mine makeBaseApp.pl -t example demo makeBaseApp.pl -t example -i demo # When prompted, use the previously created ‘demo’ make cd iocBoot/iocdemo chmod +x st.cmd ./st.cmd
Check demoApp/Db/circle.db
  Calc records ..:circle:x & ..:circle:y compute (x, y) coordinate on circle
  info() annotations create PV ”epics-dev:circle” PV as struct { angle, x, y }
PVA “epics-dev:circle” updates atomically
  camonitor epics-dev:circle:x epics-dev:circle:y receives separate x, y updates pvmonitor epics-dev:circle will always see sqrt(x2+y2)==1
  cd /ics/examples/15_pvaccess python circle.py

## Slide 16: State of PV Access in June 2026
Done, operational
PVA server for records in IOC
CS-Studio client
Area Detector images
Custom data servers and clients
  SNS: neutron data
  APS: services
Gateway
Ongoing
How to best combine data from records into custom PVA data?
Syntax for PVA links between IOC. Need global “use PVA” option
Support for IPv6
  Implemented, no operational experience
Network Security
  Can replace TCP with ‘TLS’
  Ongoing work related to certificate management

## Slide 17: History
Channel Access
PV Access
libca
C, later C++ client
pcas
C++ “portable” server
rsrv (in IOC)
C server for records
jca
Java wrapper for client
caj
Pure Java client
pyepics
Python wrapper for client
PCASpy
Python wrapper for server
qsrv
C++ server for records
pvAccessCPP
C++ server and client
pvAccessJava
Java server and client
qsrv2
C++ server for records
PVXS
C++ server and client
core.pva
Java client (and server)
pyaPy
Python wrapper
p4p
Python wrapper
Time (not to scale)
IPv6, TLS, …

## Slide 18: Summary: PV Access is ..
Update to Channel Access
  Both can be used in parallel
Similar, but supports custom data types
  Won’t replace IOC/records/normative types, but useful for special cases
Since EPICS 7 included in base IOC
  Details of ‘group’, ‘field(…)’ access still evolving
  IPv6 and network security will require PVA!