## Slide 1: EPICS Device Support Intro
Kay Kasemir
July 2026

## Slide 2: Device Support: Connect Records to Actual Hardware
IOC
read
write
AI Record
AO Record
Hardware

## Slide 3: Device Support: Connect Records to Actual Hardware
IOC
AI Record
AI Device
AO Rec.
AO Device
xxx Rec.
xxx Device
long my_read_code(aiRecord *rec) { // Somehow get value like 1234 // from hardware and place in record… rec->rval = 1234;
// Return 0 for OK,
// 2 if you set rec->val return 0; }
long my_write_code(aoRecord *rec) { // Somehow send value from record // to hardware … printf("Should set hardware to %d\n", rec->rval); return 0; }

## Slide 4: Device Support: Devil in the Details
Boilerplate to associate
  AI record with field(DTYP, “MyXXXDevice”) with long my_read_code(aiRecord *rec)
  AO record with field(DTYP, “MyXXXDevice”) with long my_write_code(aoRecord *rec)
Specific to each record type
  .. but ai, mbbi, mbbiDirect, longin, … fundamentally all handle a number, why duplicate code?
my_xxx_code must not block!

## Slide 5: Asyn: Another Layer of Abstraction
IOC
AI Record
AO Rec.
xxx Rec.
Asyn
Port Driver
Asyn acts as “Device Support”
Transfers data between “port” and records
Helpers if “port” is serial, TCP, UDP, needs to be re-opened on error

## Slide 6: Stream: Yet Another Layer of Abstraction
IOC
AI Record
AO Rec.
xxx Rec.
Asyn
Great for protocol-based devices
  Serial, TCP, UDP
  Text based, also some binary
Stream
myProtocol { out=”readVoltage”; in=“%f”; }

## Slide 7: Need to integrate an XYZ device?
Check https://epics.anl.gov/modules/index.php or https://epics-controls.org/resources-and-support/modules/hardware-support/
Ask tech-talk
   We are trying to commission an Edwards scroll pump nXDS 10i
   we have an Edwards nXDS 15i..via streamdevice
Try to use stream device
Write your own
  Check if ASYN helps. Do you want to implement
  Port Driver?
  AI, AO, BI, BO device support?