## Slide 1: Channel Finder, Name Servers
Kay Kasemir
July 2026

## Slide 2: EPICS: Distributed & loosely coupled
Start IOC  PVs are online
  No need to register IOC
  No need to reserve PV names
Like internet
  Flexibility!
  Few central bottlenecks
Start IOC  PVs are online
  No spell checker (Heartbeat…
  No “list all IOCs”, “list all PVs”
Like internet
  Chaos!
  Likely need some level of control…

## Slide 3: History: APS ‘IRMIS’, ‘crawler’
Resulting info
  Which IOC last held that record?
  When did it last boot? Where?
  Initial value of fields?
  Current value of fields?
SNS: Abandoned
  Parsing st.cmd, *.db, following ‘cd’ commands and macros is hard!
IRMIS=Integrated Relational Model of Installed Systems

## Slide 4: Channel Finder 101
Searchable list of “Channels”
Optional “Tags”
  ‘Magnet’
  ‘ImportantSetting’
Optional “Properties”
  iocNAME = ‘NameOfIOC’
  Type=‘Magnet’
  Section=‘Front End’
  Archive=‘Monitor, 00:01:00’
  Zpos = ‘10m’ (position from start of accelerator)
  Readback=‘NameOfAssociatedReadbackPV’
?!
?!
Find iocName for a PV
List all ‘Magnet’ channels
List all PVs with iocName=‘someIOC’
Get ‘Archive’ settings for PVs
Locate ‘Readback’ for some setpoint

## Slide 5
Ecosystem
Channel Finder Web Service
ElasticSearch (used to be MySQL, ca. 2009)
Operator Interface/GUI Name Lookup, Channel Table CS-Studio
RecSync All record names, IOC Name, ‘info’ tags
…
IOCs
High-Level Apps Python
cf.find(‘DTL* type=Magnet’)
Maintenance, Statistics
REST API, Shell, Python
Create Archive Config
REST API, Shell, Python
IRMIS Import

## Slide 6: Basic Setup
Install & run Elasticsearch
   Open web browser to http://localhost:9200
Install & run ChannelFinder
  Open web browser to http://localhost:8080
Install & run Recceiver (from recsync)
Instrument IOCs with reccaster (from recsync) to publish their records

## Slide 7: Instrumenting an IOC
abcApp/src/Makefile
ABC_DBD += reccaster.dbd
ABC_LIBS += reccaster
iocBoot/iocAbc/st.cmd
# Nice, but optional
epicsEnvSet("IOCNAME", "abc-ioc1")
epicsEnvSet("ENGINEER", "Fred")
epicsEnvSet("LOCATION", "Rack 123")

## Slide 8: CS-Studio: PV Name Completion
PVs from example IOC
Channel Finder demo channels

## Slide 9: CS-Studio: Channel ‘Table’
More elaborate demo data from BNL

## Slide 10: Search Options: “*Pattern* tag prop=*value*”

## Slide 11: Integration

## Slide 12: Especially useful for Disconnected Channels
What IOC is supposed to provide this channel?
When was IOC last seen?
Who to contact?
What host? Where on that host?

## Slide 13: Create you own tools
List all IOCs and their PV counts
Create archive config

## Slide 14: Elasticsearch: Count PVs
curl http://localhost:9200/channelfinder/_count?pretty
OK..

## Slide 15: Elasticsearch: List IOCs
curl -XGET "http://localhost:9200/channelfinder/_search" -H 'Content-Type: application/json' -d'
{
"query":
{
"nested":
{
"path": "properties",
"query": { "match": { "properties.name": "iocName" } }
}
},
"size": 0,
"aggs":
{
"IOCs":
{
"nested": { "path": "properties" },
"aggs":
{
"filter_ioc":
{
"filter": { "bool": { "filter": [ { "term": { "properties.name": "iocName" } } ] } },
"aggs": { "ioc": { "terms": { "field": "properties.value", "size": 500 } } }
}
}
}
} }’ Well…

## Slide 16: But it’s fast
Aggregate IOC names for 500k channels: 0.075 seconds

## Slide 17: Python: Loop over all Channels, catalog IOCs, …
Loops over 500k PVs in about 10 seconds.
Nested structure

## Slide 18: Questions
What happens when a record is removed from an IOC?
  It remains in the channel finder but as “Inactive”
How to really delete channel?
  Web interface, …

## Slide 19: Python Notebook Example

## Slide 20: Channel Finder
Database of channels
IOCs can publish their records
  With host name, contact person, ..
  ”Recceiver” tracks Active/Inactive PV status
Easy name lookup in CS-Studio
You may add other information and use in python scripts

## Slide 21: Name Servers
By default, CA or PVA Clients send PV search via UDP to “all”
  Broadcast, multicast, or (long) list of unicast addresses
Client
PV XYZ, anybody?
IOC
I have PV XYZ!
Client
Who has PV XYZ?
IOC 47
Contact IOC 47!
Name Server
Get PV XYZ
Name servers reduce the global traffic
  Search via single UDP or TCP address

## Slide 22: How does Name Server know about all PVs and IOCs?
It searches like plain client, but only once, then remembers
  https://epics.anl.gov/extensions/nameserver “learn mode” https://epics.anl.gov/icalepcs-2025/pdf/TUBR004.pdf
Add “dbl >ioc47/signal.list” to each IOC st.cmd, read those files into name server
  https://epics.anl.gov/extensions/nameserver “normal mode”
Ask Channel Finder (if you have that infrastructure in place…)
  https://github.com/ChannelFinder/cfNameserver